## Slide 1
ACSL • Unit 4 • INTERMEDIATE
🚀 ACSL Contest 4: Intermediate Division
Matrix Powers, Adders & ACSL Assembly
4-Class Master Slide Deck (4 × 90 Minutes)

## Slide 2
Unit 4 | Intermediate Division
📌 Intermediate Syllabus Matrix
• Class 1: Matrix Powers (A^k), Walks of Length k & Planarity (V-E+F=2)
• Class 2: Half-Adders, Full-Adders & Combinational Synthesis
• Class 3: Official ACSL Assembly Language Emulation
• Class 4: Contest 4 Programming Challenge & Final Comprehensive Mock
ACSL Tutoring Program • Intermediate Division • Page 2

## Slide 3
ACSL • Unit 4 • INTERMEDIATE
🌟 Class 1
The Matrix Power Walk Theorem

## Slide 4
Unit 4 | Intermediate Division
Matrix Powers Count Walks!
If A is the 0/1 adjacency matrix of graph G:
(A^k)_{i, j} = \text{The exact number of walks of length } k \text{ from vertex } i \text{ to vertex } j
Special Diagonal Property:
(A^2)_{i, i} = \text{deg}(v_i)
(In an undirected graph with no self-loops, the diagonal of A^2 gives the degree of each vertex!)
ACSL Tutoring Program • Intermediate Division • Page 4

## Slide 5
ACSL • Unit 4 • INTERMEDIATE
🌟 Class 2
Digital Adders

## Slide 6
Unit 4 | Intermediate Division
Half-Adder vs. Full-Adder
Half-Adder (Adds 2 bits A, B):
• \mathbf{\text{Sum } S = A \oplus B}
• \mathbf{\text{Carry } C = A \cdot B}
Full-Adder (Adds 3 bits A, B, C_{in}):
• \mathbf{\text{Sum } S = A \oplus B \oplus C_{in}}
• \mathbf{\text{Carry-out } C_{out} = A B + C_{in}(A \oplus B)}
Physical hardware uses 2 Half-Adders and 1 OR gate to make 1 Full-Adder!
ACSL Tutoring Program • Intermediate Division • Page 6

## Slide 7
ACSL • Unit 4 • INTERMEDIATE
🌟 Class 3
Official ACSL Assembly Language

## Slide 8
Unit 4 | Intermediate Division
The ACSL Assembly Opcodes
Opcode Meaning Action
LOAD X Load \text{ACC} = X
STORE X Store \text{memory}[X] = \text{ACC}
ADD X Add \text{ACC} = \text{ACC} + X
SUB X Subtract \text{ACC} = \text{ACC} - X
MULT X Multiply \text{ACC} = \text{ACC} \times X
DIV X Integer Divide \text{ACC} = \text{ACC} // X
BG LABEL Branch if Greater Jump if \text{ACC} > 0
BE LABEL Branch if Equal Jump if \text{ACC} = 0
BL LABEL Branch if Less Jump if \text{ACC} < 0
BU LABEL Branch Unconditional Always jump
ACSL Tutoring Program • Intermediate Division • Page 8